## Slide 1
Virginia Trout Stream Sensitivity Study
VTSSS 2021
Pink Trillium
Photo by Rob Cain
Stan Ikonen
Susie Maben
Brynna Strand
Results Summary
Rodney Minor

## Slide 2
Presentation Outline
Review of VTSSS program
Stream chemistry data/findings
Emerging threats and future climate
2021 VTSSS – Sampling summary, names and photos
Summary
Review of how acid deposition impacts fish

## Slide 3
Acid deposition and relationship to native trout stream
pH 6.0
pH 5.0
H+ and Al3+ bind to iono-regulation sites on gills
Disrupt salt and water balance in blood
H2SO4 “sulfuric acid”
SO2 “sulfur dioxide”
Al3+
Al3+
pH
H+
SO42-
SO42-
pH
H+
Carbonates- ANC
Base cations – Ca2+
Impacts developing fish
Impacts adult fish

## Slide 4
Jim Galloway
Decadal VTSSS, purpose & history
Acid emission and subsequent deposition has resulted in acidification of many streams in the Eastern US.
Brook Trout abundance
acidic moderate suitable
(silicate) (felsic) (mafic)
Data from Shenandoah National Park
Variability in bedrock composition was found to be a key control on stream response to acid deposition in Shenandoah National Park.
Mafic bedrock: well buffered, moderate pH, diverse fish species present, abundant brook trout.
Silicate bedrock: not buffered, low pH, few fish species present, less abundant brook trout.
Map source: NADP/NTN
Shenandoah National Park
1979- SWAS
Notes: Begs the question, what is the status for the entire region? Necessary to evaluate and pick sites to monitor in the long-term.

## Slide 5
Decadal VTSSS, purpose & history
Acid emission and subsequent deposition has resulted in acidification of many streams in the Eastern US.
1987 VTSSS – 367 native trout streams assessed for acid/base chemistry in VA mountains by TU, UVA and collaborators
Map source: NADP/NTN
Paul Bugas, VDWR (retired)
Rick Webb, UVA (retired)
What is the acid/base status of native trout streams throughout Virginia?

## Slide 6
Decadal VTSSS, purpose & history
VTSSS Surveys were repeated every ~10 years to assess the regional response of streams to emission/deposition reductions.
Since passing of the Clean Air Act Amendments of 1990, SO2 emissions (and deposition) have decreased by ~90%.
1987 - 367 sites sampled
2000 - 445 sites sampled
2010 - 455 sites sampled
2021 – 454 sites sampled

## Slide 7
Volunteer Sample Site Map
Sample Window: Last week of April 2021

## Slide 8
VTSSS 2021 sample collection summary
1 state TU coordinator: Tom Benzing
Northern VA regional coordinator: Marcia Woolman
13 TU Chapters and Coordinators (+ Bath and Highland County)
Each Chapter sampled 12-45 sites
155 volunteers, 383 sites (+ 71 additional quarterly) = 454 sites sampled
Volunteer hours reported: 1150 hrs
  Skyline – Steve Romine
  Smith River – Wayne Kirkpatrick /Eric Tichay
  Little Stony – Justin Bently
  Mountain Empire – Heather Davidson
  New River – Arnold Graboyes
  Southern WVA – Chris Mullins/Steve Pugh
  Highland/Bath County – Rick Webb/ Ryan Hodges
  Northern VA – Rob Cain/Chris Rich
  Rapidan- Amy Orr
  Winchester- Stan Ikonen
  Massanutten – Rodney Miner
  Shenandoah Valley – Tom Benzing
  Roanoke – Mark Taylor
  Thomas Jefferson – Chubby Damron

## Slide 9
Notable Repeat Volunteer Samplers (based on field forms)
2021 TU Chapter
Name
Years sampled (1987, 2000, 2010, 2021)
Rapidan Andy Holmaas 1987, 2000, 2010, 2021
Roanoke Valley Jeff Cutright 1987, 2000, 2021
Shenandoah Valley Doug Stegura 2000, 2010, 2021
Rapidan Marcia Woolman 2000, 2010, 2021
Smith River Rusty Lacy 1987, 2021
Most Sites Sampled by an individual/family in 2021
Mountain Empire Lisa Benish 15 sites!
Thomas Jefferson Chubby Damron & Jaydon Damron 12 & 2 sites
Mountain Empire Heather, Kevin, Kaydee Davidson 10 & 9 & 8 sites

## Slide 10
VTSSS 2021
Thanks to all those who sampled!

## Slide 11
Rob Cain photograph/flower ID
Pink trillium grandiflorum
Trillium grandiflorum
chickweed
bluets
Solomon’s seal
Wild geranium
violet

## Slide 12
VTSSS 2021
Thanks to all those who coordinated and delivered samples!
Arnold Graboyes, New River
Chubby Damron, TJ
Eric Tichay, Smith River
Heather Davidson, Mountain Empire & Little Stony, S. West Va
Marcia Woolman,
Northern Chapters
Mark Taylor,
Roanoke Valley
Rick Webb, Highland & Bath County
Rodney Minor, Massanutten
Steve Romine, Skyline
Tom Benzing, Shenandoah Valley

## Slide 13
Acid-neutralizing capacity (ANC)
ANC is a general measure of stream sensitivity to acid and is used to classify streams as suitable or unsuitable for Brook Trout
pH
pH is a more direct measure of current stream conditions and has biological implications
Stream chemistry data in this presentation include:
UVa VTSSS Laboratory
SO4 2-
Sulfate is the main acidifier from acid deposition
NO3 -
Nitrate, also acidifies but typically very low in VA mountain forest streams
Sum of Base Cations (SBC)
SBC (Calcium + Magnesium+ Sodium+ Potassium)
Weathering products from bedrock that neutralize acid inputs.

## Slide 14
ANC thresholds and Brook Trout response
ANC concentrations will be presented by their associated brook trout response category, as listed in the table

## Slide 15
2021 Acid Neutralizing Capacity (ANC) by ‘response category’

## Slide 16
1987
2000
2010
Brook Trout Response Category for each of the VTSSS decadal surveys
Chart: 1987 - ANC
| Unsuitable | Marginal | Intermediate | Suitable
 | 4.9046 | 11.7166 | 25.6131 | 57.7657
2021
Chart: 2000 - ANC
| Unsuitable | Marginal | Intermediate | Suitable
 | 3.5955 | 11.236 | 22.6966 | 62.4719
Chart: 2010 - ANC
| Unsuitable | Marginal | Intermediate | Suitable
 | 5.0549 | 8.7912 | 14.7253 | 71.4286
Chart: 2021 - ANC
| Unsuitable | Marginal | Intermediate | Suitable
 | 3.0769 | 11.6484 | 16.044 | 69.011
We have observed increases in the percentage of sites with suitable habitat, between 1987 and 2021.
The percent of sites with unsuitable habitat has decreased between 1987 and 2021.
Median
ANC
62 69 94 85

## Slide 17
Some bedrock types can more easily neutralize acids
  Mafic high ANC, not sensitive to acidification (29 sites)
  Felsic (104 sites)
  Argillaceous (105 sites)
  Siliciclastic low ANC, very sensitive to acidification (215 sites)
Bedrock class for VTSSS 2021 sites
least sensitive
most sensitive
Notes: USFS – 305 sites, NPS 65 sites, 87 sites other designation

## Slide 18
50
For sites on each bedrock class, we observe improvements in median ANC from 1987-2010, but not between 2010 and 2021.
Suitable
ANC, for each survey year, grouped by bedrock
1987 2021
1987 2021
1987 2021
1987 2021
least sensitive most sensitive

## Slide 19
Sulfate, for each survey year, grouped by bedrock
For sites on each bedrock class, we observe improvements (decreases) in median sulfate from 1987 to 2021.
Sulfate decreases in streamwater are more moderate than rainwater (~38 to 3 µeq/L), due to years of accumulation in soils.
SHEN Precip

## Slide 20
Nitrate, for each survey year, grouped by bedrock
In 2021, increases in nitrate in 2021 (~15 µeq/L) observed. Potential reasons for increase in nitrate include watershed disturbance (e.g., defoliations/pests).
Nitrate concentrations in precipitation in SHEN have decreased between 1987 and 2020, from 16 to 5 µeq/L.
SHEN Precip

## Slide 21
Sum of Base Cations, for each survey year, grouped by bedrock
For sites on each bedrock class, we observe increases in median SBC from 1987-2010, but not from 2010 to 2021 (except Mafic), like ANC trends.

## Slide 22
ANC trends, 1987-2021
The trend in ANC from 1987-2021 indicates a range in recovery rates for individual sites within a bedrock class.
Mafic sites have a greater median increasing rate of ANC.
Median ANC, µeq/L/yr
1.6 0.7 0.7 0.4
Faster Recovery
Slower Recovery

## Slide 23
Do stream chemical trends relate to watershed characteristics?
Watershed Characteristics
Latitude
Longitude
Area
Mean Leaf Area Index
Mean Annual Precipitation
Min elevation
Max elevation
Mean elevation
Mean Slope
Mean Aspect (east/west and north/south)
% Forest Cover
There is variability in chemical trends over time.
Is there a relationship to watershed characteristics?
Mean/Max watershed elevation is the most consistent predictor variable for trends for all sites and individual bedrock groupings.
Lower elevation sites are recovering faster
Faster Recovery
Slower Recovery

## Slide 24
Nitrate trends – relationship to watershed characteristics
There is a strong significant relationship between nitrate trends and watershed Latitude. Northern sites had greater increases in nitrate.
We do not know the reason for this trend yet.
Potential for forest pests, concentrated regionally, to be impacting health and nutrient uptake of forest.

## Slide 25
Summary
Chemical conditions (ANC) in Appalachian mountain streams that support native brook trout have improved for the majority of sites (~86%) between 1987 and 2021.
Despite improvements, only 69% of streams have ANC levels that are consistently ‘suitable’ for brook trout.
Declines in stream water sulfate concentrations, driven by emission regulations initiated with the 1990 Clean Air Act Amendments, contribute to improvements in stream chemistry.
Sites with mafic bedrock and those at lower elevations are recovering at a faster rate.

## Slide 26
Environmental Protection Agency – Clean Air Markets Division, assesses response to acid rain in US
Virginia Department of Environmental Quality
Data dissemination
Regulators
Resource Managers and Scientists
Public
National Park Service –Evan Childress, supervisory fisheries biologist
U.S. Forest Service – Dawn Kirk, fisheries biologist for GW and Jefferson NF
Virginia Department of Wildlife Resources – Steve Reeser, fisheries biologist
Public, via the SWAS-VTSSS website and federal database (Water Quality Portal)
Teachers
Students
Citizen scientists
Fisherman
…

## Slide 27
SWAS-VTSSS Mountain Stream Database
https://swas.evsc.virginia.edu/POST/scripts/overview.php

## Slide 28
Looking towards the future environment…

## Slide 29
Emerging threat: Microplastics
Microplastic under blue light
Matthew Zaragoza, 4th-year UVA student
Biological effects on fish:
Accumulates in digestive track and liver
Obstructs gills
Increase mercury bioaccumulation
Prevent nutrient assimilation
Carriers for organic pollutants, heavy metals, pesticides, and harmful pathogens

## Slide 30
Emerging threat: Microplastics
Results
194 samples collected
122 stream samples analyzed
23% have microplastics in a 1L sample
~0.26 microplastic pieces per L in VA mountain streams
BASELINE DATA important to understanding future changes
Sampling added to VTSSS in 2021.

## Slide 31
Multiple Environmental Stressors: a changing climate combined with slow recovery from acid emission/deposition
Increasing stream temperature
- caused by increasing air temperature
- caused by a decrease in stream shading
The brook trout’s very name reflects its vulnerability. “Fontinalis” means “of the springs,” revealing the species’ reliance on cool, clear water to survive.

## Slide 32
Projections for a changing climate
Temperature > 20ºC
ANC < 50 µeq/L
downstream
Habitat
upstream
Changes in streamflow may have mixed effects (Blum et al. 2019)
  Increased fall and summer baseflows are beneficial
  Higher intensity storms may harm eggs and juveniles in winter and spring
Downstream warming and headwater acidity may diminish cold water habitat (McDonnell et al. 2015)
  2 -4°C air temperature increase = 6%- 10% reduction in cold water habitat in SE US forests

## Slide 33
Thank you for participating and listening!
And thank you to our funders (47.1K raised)
Individual donations!